## Slide 1: Basic IO Interfacing on Firebird-V

## Slide 2: What Are Ports
Juncions where peripheral devices are connected.
Peripheral devices can be
Input Device
Example: Switch, Sensors, etc...
Output Device
Example: Buzzer,LCD,Motors,LED, etc...

## Slide 3
PORTS in ATmega 2560
1
ATmega2560 is a 100 pin micro-controller.
2
86 pins can be used as Input/Output pins.
3
Pins are grouped together and called as Port.
ATmega2560 has ten 8-bit Ports
Port x; x = A to F and H,J,K,L
ATmega2560 has one 6-bit port Port G;
All Port pins can be configured individually as Input/Output.

## Slide 4
Accessing Ports
Each Port has three associated registers with it:
1
DDRx x = A to H and J,K,L
PORTx x = A to H and J,K,L
PINx x = A to H and J,K,L
2
3
5/18

## Slide 5
Outline Input-Output Ports in ATmega2560 Write Your First Embedded C Program
Overview of Ports Acessing Ports Examples
Understanding DDRx Register
1
Data Direction Register
2
Purpose: To set Port pins as Input/Output
DDRx= 0 : Port x is defined as Input.
DDRx= 1 : Port x is defined as Output.
3
Example: For Port B, make lower nibble as Input and upper nibble as Output.
DDRB=
DDRB= 0xF0
www.e-yantra.org
Firebird ATmega2560 Robotics Research Platform
6/18

## Slide 6
Outline Input-Output Ports in ATmega2560 Write Your First Embedded C Program
Overview of Ports Acessing Ports Examples
Understanding DDRx Register
1
Data Direction Register
2
Purpose: To set Port pins as Input/Output
DDRx= 0 : Port x is defined as Input.
DDRx= 1 : Port x is defined as Output.
3
Example: For Port B, make lower nibble as Input and upper nibble as Output.
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
DDRB=
DDRB= 0xF0
www.e-yantra.org
Firebird ATmega2560 Robotics Research Platform
6/18

## Slide 7
Outline Input-Output Ports in ATmega2560 Write Your First Embedded C Program
Overview of Ports Acessing Ports Examples
Understanding PINx Register
1
Purpose: To read data present on Port x pins.
2
Save the value of register in a variable
3
Example:
Read Data from PORTC
PORTC =
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
x= PINC
x=0xF0
www.e-yantra.org
Firebird ATmega2560 Robotics Research Platform
7/18